## Slide 1: F5 Fiberbundle HDF5
Werner Benger
Center for Computation & Technology
Louisiana State University
http://sciviz.cct.lsu.edu/

## Slide 2: Abstract
“The proper abstractions for scientific data are known. We just have to use them.” (D. M. Butler & S. Bryson, 1992): There is no common standard or agreement on file formats for scientific data, but there could be. The inductive approach common in software development usually leads to “special solutions for special problems” which are extended on a case by case basis. Consequently, each application develops their own approach of describing data, ultimately leading to incompatibilities in the file formats associated with these applications and groups of applications. In contrast, the deductive approach to describe data based on the theory of fiber bundles leads to a generalized way of describing scientific data independent of a particular scientific domain or application as it exhibits the mathematical abstractions that are common across disciplines.
This presentation will review the “F5” approach of modeling data for scientific visualization using fiber bundles on top of HDF5 as underlying I/O layer. The F5 model has originally been developed about 12 years ago in the context of numerical relativity simulation data as produced by Cactus, for handling both primary simulation (uniform grids, adaptive meshes, curvilinear grids, multipatch data…) and secondary post-processing data (surfaces, lines, particle sets, …). The formalism and implementation itself is independent of Cactus and has since been applied to other domains such as medical imaging, computational fluid dynamics (CFD), smoothed particle hydrodynamics (SPH) and geoscience data, easing scientific visualization through this common denominator. The presentation will provide a short review of the basic concepts and provide an in-depth discussion on how the F5 model describes various common and less common data types.

## Slide 3: Overview
    The Problem
    Mathematics for Visualization
    The Fiber Bundle data model
    HDF5
    Mapping the Fiber Bundle model to HDF5
      Basics
      Extensions
      F5 API

## Slide 4
Thanks to Mark Miller, LLNL

## Slide 5: Data Types
Point Sets
Unstructured Cell Data
Tetrahedral Grids
Regular Grids
Uniform Grids
Uniform Cartesian Grids
Uniform Polar Grids
…
Triangular Surfaces
Quad-based Surfaces
Irregular Surfaces
Hierarchical Grids (AMR)
Streamlines, Particle Trajectories, Geodesics
Apparent Horizons
Embedding Surfaces
…

## Slide 6: “Special problems need special solutions”
Inductive approach in software engineering leads to incremental advances starting from a specific problem
Solutions often implemented on an enumerated case-by-cases basis
 Results in many independent solutions

## Slide 7: Interoperability?
Amira
AVS
Visit/Paraview
OpenDX
Vish

## Slide 8: Data Model in SciViz
No commonly agreed data model exists for scientific visualization!
Data can not be shared among different visualization software!

## Slide 9: Interoperability… wishful thinking
Amira
AVS
Visit/Paraview
OpenDX
Vish

## Slide 10: Interoperability
N Applications
M File Formats
Amira
Visit
Scirun
Ensight
OpenDX
DICOM
Cactus
CGNS
NetCDF
GeoTIFF
Diverse Visualization Software ↔ Data sets in diverse file formats

## Slide 11: N x M Implementation Effort
n applications, m file formats
Amira
Visit
Scirun
Ensight
OpenDX
DICOM
Cactus
CGNS
NetCDF
GeoTIFF

## Slide 12: N + M Common Data Model
n sources, m sinks, 1 route
Amira
Visit
Scirun
Ensight
OpenDX
DICOM
Cactus
CGNS
NetCDF
GeoTIFF
Common Data Model

## Slide 13: Commonalities of Grid types
Regular Grid
Uniform Grid
Rectilinear Grid
Curvilinear Grid

## Slide 14: Hierarchy of Grid types
Regular Grid
Uniform Grid
Rectilinear Grid
Curvilinear Grid
Point Sets
Irregular Grids
Lines
Triangular Surfaces
Tetrahedral Grids

## Slide 15: Challenge of a Common Data Model
“The proper abstractions for scientific data are known. We just have to use them.”
D. M. Butler & S. Bryson
Vector-Bundle Classes form Powerful Tool for Scientific Visualization
Computers in Physics, Vol. 6, No 6., Nov/Dec 1992

## Slide 16: Motivation
Elegant mathematical formulations inspire visualization methods to become
  More general
  Wider applicable
  Better structured, more modular
Deductive Approach
  Methods (I/O, numerical algorithms, visualization) are implemented with the broader context in mind

## Slide 17: Mathematics for Visualization
Topology
Discretization schemes, combinatorial structure, relational information
Differential Geometry
Coordinate representations, transformations, differential operators, tensor algebra
Geometric Algebra
N-dimensional Rotations, navigation, data analysis, feature extraction, spinor formalism, generalized quaternions, mimetic operators

## Slide 18: Topology
Concept of fiber bundles
Concept of cw-complexes and k-Skeletons
Relational Information

## Slide 19: Fiber Bundles: Unification of data types

## Slide 20: Mathematical Definition
Let E, B be topological spaces and f : E → B a continuous map.
(E,B,f) is called a (fiber) bundle if there exists a space F such that the union of fibers of a neighborhood UbB of each point bB are homeomorphic to UbF such that the projection pr1 of Ub  F is Ub again.

## Slide 21: Naming
E is called the total space E,
B is called the base space,
f : E → B the projection map.
The space F is called the fiber of the bundle.
(E,B,f: E→B) bundle F : bB : UbB : f−1 (Ub) ≃ UbF
and pr1(Ub  F) = Ub

## Slide 22: A Fiber Bundle Homeomorphism

## Slide 23: A Non-Fiber Bundle Homeomorphism

## Slide 24: Fiber Bundle Data Model
Is a generic approach to handle a wide range of data types used for scientific visualization
Basic concept: Base space maps to fibers
Base Space
Fiber Space at each
point of Base Space

## Slide 25: Total Space for Data in SciViz
Base Space
Discretized
  Neighborhood, Connectivity, k-Skeletons
  Described via integer-valued arrays referring to indices
  Numerical values are intrinsic, no dependence on coordinate system
Fiber Space
Continuous
  Scalar, vector, tensor fields
  Described via float point numbers
  Numerical value depends on representation (coordinate system)
    Exception: true scalar fields

## Slide 26: “F5 Fiber Bundle Data Model”
A property-based description of scientific data
A specific data type is built from “construction blocks” (not enumerated case lists)
Does not answer the question “what is it?” but answers the question(s) “how is it?”
A specific data set can have properties of many data types
  non-exclusive properties
  eases/enhances interoperability
Enables abstract operations independent of data type

## Slide 27: The F5 Fiber Bundle Data Model
Fiber Bundle
Casts data into hierarchy:
T=0.0
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle

## Slide 28: Lowest Level: Fiber Bundle over a Parameter Space
Similar to 3+1 Decomposition in Numerical Relativity
Time
Fiber Bundle
T=0.0
T=0.4
T=0.8
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle
T=0.0
T=0.4
T=0.8

## Slide 29: Grid: A geometric entity
Fiber Bundle
T=0.0
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle

## Slide 30: Grid Objects as Fibers of a two-dimensional Parameter Space
Evolutions and Identifiers
Fiber Bundle
T=0.0
T=0.4
T=0.8
Time
Grid Identifier

## Slide 31: Grid Iterations
Iterate over 1st dimension “time”:
Find all Grid objects that exist for a specific instance of (physical) time or time interval
Iteration by physical time, not “time-step”
Iterate over 2nd dimension “Grid ID”
Find all times for which a Grid exists
Temporal evolution of a Grid and its data
Allows to trace features in Grid objects
Generalization of one-dimensional “time” to higher-dimensional parameter spaces possible
 Easy synchronization of distinct data sources
Compare an ensemble of simulations

## Slide 32: Structure of a Grid Object
Consider discrete base space:
Definition “k-cell”
Definition “incident”
Definition “adjacent”
Definition “n-Skeleton”
Definition “CW-Complex”

## Slide 33: Topology: cw-Complex
Discretized n-dimensional Manifold
Concept of k-cells with adjacency
Hierarchy of k-Skeletons, k=0…N
  0-cell: Vertices 1-cell: Edges 2-cell: Faces 3-cell: simplexes

## Slide 34: Definition “incident”
Two cells c1, c2 are incident if c1  ∂c2, where ∂c2 denotes the border of the cell c2.
Two cells of the same dimension can never be incident because dim(c1) ≠ dim(c2) for two incident cells c1, c2.
c1 is a side of c2 if dim(c1) < dim(c2), which may be written as c1 < c2.

## Slide 35: Definition: “adjacent”
Two k−cells c1, c2 with k > 0 are called adjacent if they have a common side, i.e.
cell c1, c2 adjacent   cell f : f<c1 , f<c2 .
For k = 0 two 0-cells (i.e. vertices) v1, v2 are said to be adjacent if there exists a 1-cell (edge) ℮ which contains both, i.e. v1 < ℮ and v2 < ℮.

## Slide 36: Formal Definition: Skeleton
A decomposition of a Hausdorff space X, is a hierarchical system of spaces X(−1)  X(0)  X(1)  …  X(n), constructed by pairwise disjoint open cells c  X with the Hausdorff topology, such that X(n) is obtained from X(n−1) by attaching adjacent n-cells to each (n − 1)-cell and X(−1) = ∅.
The respective subspaces X(n) are called the n-skeletons of X.

## Slide 37: CW-Complex
A decomposition is also called a CW-complex.
It can be understood as a set of cells which is glued together at their subcells.
It is a generalization of the concept of a graph by adding cells of dimension greater than 1.

## Slide 38: Topology: k-Skeletons
Edges
Faces
Fiber Bundle
T=0.0
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle

## Slide 39: Extended Skeletons
Refinement Levels
  Multiresolution, Adaptive Mesh Refinement
Cell Complex
  Blocks, fragments
Topological Relationships
  Grid future/past
  Intergrid Relationships

## Slide 40: Differential Geometry
Concept of a manifold and charts
Data
Cartesian
Coordinates
Spherical
Coordinates

## Slide 41: Structure of the Fiber Space
May carry
  Scalar fields
  Vector fields
  Covector fields
  Tensor fields
  Pseudo-scalars
  Multi-Vectors
  Non-tensorial geometrical objects (e.g., Christoffel symbols)

## Slide 42: Special cases of fiber space
Has vector space property:
  E.g. contains vectors, tensors:
     Vector Bundle
Is the tangent space of a manifold M:
     Tangent Bundle M × T(M)

## Slide 43: Representation
Numerical representation via coordinates:
  A manifold M is an Hausdorff space with (local!) maps x:Mℝn.
  x={x0,x1,x2…xn-1} is called a chart
  xm:Mℝn the mth coordinate function
A chart in the base manifold M induces a coordinate basis in the tangential space.

## Slide 44: Multiple Representations
Fiber Bundle
T=0.0
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle

## Slide 45: Geometric Algebra: Vectors, Tensors, Spinors, …
Fiber Bundle
T=0.0
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle

## Slide 46: Access via Parameters
Fiber Bundle
T=0.0
Grid
Vertices
Cartesian
Coordinates
Field
Time
Gridname
Topological property
Coordinate system
Fieldname

## Slide 47: Grids and Fields
End-user operates only on Grid objects and Fields
Velocity
Pressure
Temperature
Density
Energy

## Slide 48: Application Example: Multiblock Curvilinear Data
The Stirtank Dataset
    2088 curvilinear blocks
    5000 time steps
    Vectorfield describing velocity
    Scalarfield describing pressure
    500GB Binary Data

## Slide 49: Streamlines

## Slide 50: Streamlines in the Fiber Bundle
Model all Data within the
  Fiber Bundle Model
   Grid objects, Field objects
Out: Grid
In: Field
In: Grid
Streamlines
Computation
Vector Field
Seed Points
Set of Lines

## Slide 51: “Convolution” of Grids
Replicate Grid by points on another Grid
Out: Grid
In: Grid
In: Grid
Grid
Convolver
Point
Distribution
Seed Points
Marcel Ritter, 2006

## Slide 52: Systematic Approach
In: Grid
Out: Grid
In: Bundle
Out: Grid
In: Grid
Out: Field
In: Field
Out: Grid
In: Grid
Out: Grid
In: Grid
F5 Data
Bundle
Grid Selector
Vector Field
Grid Convolver
Streamlines
Computation
Line Renderer
Input - Grid
…
Out: Grid
In: Grid
Grid Convolver
    Grid objects and Fields as entities within a visualization environment

## Slide 53: Systematic Approach
In: Grid
Out: Grid
In: Bundle
Out: Grid
In: Grid
Out: Field
In: Field
Out: Grid
In: Grid
Out: Grid
In: Grid
F5 Data
Bundle
Grid Selector
Vector Field
Grid Convolver
Streamlines
Computation
Line Renderer
Input - Grid
…
Out: Grid
In: Grid
Grid Convolver
    Grid objects and Fields as entities within a visualization environment

## Slide 54: Systematic Approach
In: Grid
Out: Grid
In: Bundle
Out: Grid
In: Grid
Out: Field
In: Field
In: Grid
Out: Field
In: Grid
F5 Data
Bundle
Grid Selector
Vector Field
Scalar Field
Streamlines
Computation
Line Renderer
Out: Grid
In: Field
Isosurface
    Seeding Streamlines from an Isosurface

## Slide 55: F5 – Fiber Bundle HDF5
F5 as file format and I/O library

## Slide 56: HDF = Hierarchical Data Format
HDF5 is the second HDF format
  Development started in 1996
  First release was in 1998
  http://www.hdfgroup.org
Designed for HPC simulations
High-performance, large data, long-term data preservation (archival), portability
F5:Casting Fiber Bundle Data Model into HDF5

## Slide 57: HDF5 File
lat | lon | temp
----|-----|-----
12 | 23 | 3.1
15 | 24 | 4.2
17 | 21 | 3.6
An HDF5 file is a container that holds data objects.
Experiment Notes:
Serial Number: 99378920
Date: 3/13/09
Configuration: Standard 3

## Slide 58: Structures to organize objects
palette
Raster image
3-D array
2-D array
Raster image
lat | lon | temp
----|-----|-----
12 | 23 | 3.1
15 | 24 | 4.2
17 | 21 | 3.6
Table
“/” (root)
“/foo”
“Groups”
“Datasets”
Notes: This shows that you can mix objects of different types according to your needs. Typically, there will be metadata stored with objects to indicate what type of object they are.
Like HDF4, HDF5 has a grouping structure. The main difference is that every HDF5 file starts with a root group, whereas HDF4 doesn’t need any groups at all.

## Slide 59: HDF5 Groups and Links
lat | lon | temp
----|-----|-----
12 | 23 | 3.1
15 | 24 | 4.2
17 | 21 | 3.6
Experiment Notes:
Serial Number: 99378920
Date: 3/13/09
Configuration: Standard 3
/
SimOut
Viz
HDF5 groups and links organize data objects.

## Slide 60: Path to HDF5 object in a file
“/”
X
temp
temp
  / (root)
  /X
  /Y
  /Y/temp
  /Y/bar/temp
Y
bar
Notes: Like HDF4, HDF5 has a grouping structure.
The main difference is that every HDF5 file starts with a root group, whereas HDF4 doesn’t need any groups at all.

## Slide 61: Example Dataset
The internal HDF5 file organisation made visible using the h5ls command: h5ls –rv file.h5
/Block00001 Dataset {5/5, 13/13, 9/9}
Location: 1:15768
Links: 1
Storage: 7020 allocated bytes
Type: struct {
"x" +0 native float
"y" +4 native float
"z" +8 native float
} 12 bytes
Data:
(0,0,0) {0.210951, -0.0406732, 0.0611351},
{0.210204, -0.0443333, 0.0611199},
{0.209324, -0.0483009, 0.0611070},
{0.208286, -0.0525892, 0.0610958}
(0,0,4) {0.207065, -0.0571980, 0.0610863},
{0.205640, -0.0621138, 0.0610815},
HDF5 allows easily to attach
names to the numerical values.
HDF5 takes care of endianess, double to float
conversion and different layouts, e.g.
{x,y,z} vs {z,x,y}
The naming scheme can also serve
to identify the coordinate system rel.
to which the numbers are stored
e.g. {x,y,z} vs {r, phi, theta}

## Slide 62: HDF5 as a file system in a file
HDF5
File System
Group
Dataset
  Size
  Creation date
  Dimensionality
  Data type (int, float, …)
Symbolic Link
Attributes
Named data types
Mounting external data
Virtual File Driver (stdio, mpi-io, streaming VFD,…)
Directory, Folder
File
  Size
  Creation data
  -
  -
Symbolic Link, Shortcut
-
-
Mounting file systems
File system type (ext3, ntfs, nfs,…)

## Slide 63: F5 File Format
Fiber Bundle
Casting 6 hierarchy levels into HDF5
T=0.0
Grid
Vertices
Coordinates
Field
Field
Representation
Skeleton
Grid object
(Time) Slice
Bundle

## Slide 64: /Time/Grid/Top/Rep/Field/
h5ls -r minkowski-0000.f5
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::LAPSE Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0.119047619047619041010577234374 Group
/T=0.119047619047619041010577234374/minkowski Group

## Slide 65: F5 Hierarchy in HDF5
Time Slices (parameter space)
Grid (geometrical entity)
Topology  n-Skeletons
Representation (coordinate systems,
Field (denotes data sets)
Field fragments (denotes data layout)
Compound component (alternative layout for compound data)

## Slide 66: /Time/Grid/Top/Rep/Field/Fragment
Slicing of a spacetime
Bundles all entities that belong to a certain physical time
Encompasses all information that might relates to a certain time
May contain multiple geometries
Constraints on HDF5 file:
  No datasets contained on this level
  Group must have floating-point attribute “time”

## Slide 67: Example: h5ls -r
h5ls -r minkowski-0000.f5
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::LAPSE Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dz Dataset {43, 37, 19}
/T=0.119047619047619041010577234374 Group
/T=0.119047619047619041010577234374/minkowski Group

## Slide 68: /Time/Grid/Top/Rep/Field/Fragment
Description of a geometrical entity
Bundles all properties that belong to a certain object
Encompasses all information that is or might be required to perform operations on the certain object
… is a spatial manifold (or topological space) plus fiber space
Constraints on HDF5 file:
  No datasets contained on this level
  Group must have at least one subgroup fulfilling the constraints of a “Vertex Skeleton”

## Slide 69: Example: h5ls -r
h5ls -r minkowski-0000.f5
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::LAPSE Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dz Dataset {43, 37, 19}
/T=0.119047619047619041010577234374 Group
/T=0.119047619047619041010577234374/minkowski Group

## Slide 70: /Time/Grid/Top/Rep/Field/Fragment
Topological properties of a Grid
One entry for each k-Skeleton:
  Vertices, Edges, Faces, Cells
Contains Index spaces:
  Discrete sets with properties
    Color per vertex, color per face, color per cell
  Cell Complexes: sets of cells
Constraints on HDF5 file:
  Attribute “index depth”
  All datasets in this group or below must have same number of elements and dimensionality
  Optional attribute “refinement”

## Slide 71: Example: h5ls -r
h5ls -r minkowski-0000.f5
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::LAPSE Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dz Dataset {43, 37, 19}
/T=0.119047619047619041010577234374 Group
/T=0.119047619047619041010577234374/minkowski Group

## Slide 72: /Time/Grid/Top/Rep/Field/Fragment
Representation of Skeleton relative to “something”, e.g.:
  Charts (coordinate systems)
  N-Skeletons (cells as vertices, faces as vertices, vertices as cells)
  Cell complexes (cells per complex, complexes per cell)
  Another Grid (interpolation weight)
Constraints on HDF5 file:
  The name of the group must refer to an existing entity, such as a coordinate system identifier or another Skeleton group

## Slide 73: Example: h5ls -r
h5ls -r minkowski-0000.f5
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::LAPSE Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dz Dataset {43, 37, 19}
/T=0.119047619047619041010577234374 Group
/T=0.119047619047619041010577234374/minkowski Group

## Slide 74: /Time/Grid/Top/Rep/Field/Fragment
A set of numerical values
Positional information in the base space
  Vertex coordinates or vertex indices per cell
Field data in the fiber space
  Scalar, vector, tensor, …
  Color per cell, color per vertex
Constraints on HDF5 file:
  An entries may be n-dimensional dataset or a group; if it is a group, it needs to be identifiable as either
    Fragmented field (contains sequence of n-dimensional datasets)
    Compound data type with k separated components (contains k n-dimensional scalar-valued datasets)
    Compound data type constructed as direct product of components (contains n one-dimensional scalar-valued datasets)
    Linear field or polynomial expression

## Slide 75: Procedural fields
Storage of field via group with attributes instead of dataset
Value per point computed procedurally on demand
Examples:
  Equidistant coordinates (linear map of index to coordinate values)
  Storage of compound data as separated components (XYZXYZ  XXYYZZ)

## Slide 76: Special Field Names
Reserved field name “Positions”
Stores coordinate locations
  Coordinates in physical space
    Cartesian,
    Spherical
    Cylindrical
  Coordinates in index space
    Vertex indices per cell
    Edges per cell

## Slide 77: Example: h5ls -r
h5ls -r minkowski-0000.f5
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::CURV/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::LAPSE Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS Group
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/STATICCONFORMAL::CONFAC_1DERIVS/Dz Dataset {43, 37, 19}
/T=0.119047619047619041010577234374 Group
/T=0.119047619047619041010577234374/minkowski Group

## Slide 78: Multiple Coordinate Systems
/T=0/minkowski/Points/StandardCartesianChart3D Group
/T=0/minkowski/Points/StandardCartesianChart3D/Positions Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxx Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gxz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyy Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gyz Dataset {43, 37, 19}
/T=0/minkowski/Points/StandardCartesianChart3D/ADMBASE::METRIC/gzz Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D Group
/T=0/minkowski/Points/SphericalChart3D/Positions Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC Group
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC/grr Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC/grp Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC/grh Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC/gpp Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC/gph Dataset {43, 37, 19}
/T=0/minkowski/Points/SphericalChart3D/ADMBASE::METRIC/ghh Dataset {43, 37, 19}

## Slide 79: /Time/Grid/Top/Rep/Field/Fragment
Internal memory layout of a field
Field may be stored
  as contiguous block
  as multiple sub-blocks (e.g. from domain decomposition)
Layout information may be shared among fragments
  Coordinate location/boundaries of each fragment

## Slide 80: Howto…
Specify relative information
  Vertices per triangle, triangles per vertex, vertices per edge, edges per vertex, ..
Specify hierarchical meshes
Specify interpolation weights between grids
Define clusters of cells, edges, …
Trace time-dependent changes
Specify partially time-independent data

## Slide 81: Concept of “Index Depth”
An integer property of an index space (Skeleton object), similar to dimensionality
  Dimensionality: intrinsic property
  Index depth: extrinsic property
Describes “how far” the index space is from the primary (mandatory) Vertex information of a Grid:
  0  Vertices
  1  Edges, Faces, Tetrahedrons, …
  2  Groups of edges, faces, tetrahedrons
  3  Groups of elements of index depth 2
  4  Groups of 3-elements
  …

## Slide 82: Relative Representations
/T=1 Group
/T=1/adcirc Group
/T=1/adcirc/Points Group
/T=1/adcirc/Points/StandardCartesianChart3D Group
/T=1/adcirc/Points/StandardCartesianChart3D/Positions Dataset {314442}
/T=1/adcirc/Connectivity Group
/T=1/adcirc/Connectivity/Points Group
/T=1/adcirc/Connectivity/Points/Positions Dataset {600331}
Triangular Surface: 600331 Triangles, 314442 Points
Index Depth = 0
Index Depth = 1

## Slide 83: Relative Representations
/T=1 Group
/T=1/adcirc Group
/T=1/adcirc/Points Group
/T=1/adcirc/Points/StandardCartesianChart3D Group
/T=1/adcirc/Points/StandardCartesianChart3D/Positions Dataset {314442}
/T=1/adcirc/Points/Connectivity/Positions Dataset {314442}
/T=1/adcirc/Connectivity Group
/T=1/adcirc/Connectivity/Points Group
/T=1/adcirc/Connectivity/Points/Positions Dataset {600331}
Inverse Information: Triangles per Vertex

## Slide 84: Fields on Relative Representations
/T=1 Group
/T=1/adcirc/Connectivity Group
/T=1/adcirc/Connectivity/Points Group
/T=1/adcirc/Connectivity/Points/Positions Dataset {600331}
/T=1/adcirc/Points Group
/T=1/adcirc/Points/StandardCartesianChart3D Group
/T=1/adcirc/Points/StandardCartesianChart3D/Positions Dataset {314442}
/T=1/adcirc/Points/StandardCartesianChart3D/elevation Dataset {314442}
/T=1/adcirc/Points/StandardCartesianChart3D/vector Dataset {314442}
Triangular Surface: 600331 Triangles, 414442 Points
plus data on the vertices

## Slide 85: Relative Representations
/T=1 Group
/T=1/adcirc/Connectivity Group
/T=1/adcirc/Connectivity/Points Group
/T=1/adcirc/Connectivity/Points/Positions Dataset {600331}
/T=1/adcirc/Connectivity/StandardCartesianChart3D/elevation Dataset {600331}
/T=1/adcirc/Connectivity/StandardCartesianChart3D/vector Dataset {600331}
/T=1/adcirc/Points Group
/T=1/adcirc/Points/StandardCartesianChart3D Group
/T=1/adcirc/Points/StandardCartesianChart3D/Positions Dataset {314442}
Triangular Surface: 600331 Triangles, 414442 Points
plus data on the triangles

## Slide 86: Unstructured Meshes
Skeletons and Primary Representations:
/T=1 Group
/T=1/adcirc Group
/T=1/adcirc/Points Group
/T=1/adcirc/Points/StandardCartesianChart3D Group
/T=1/adcirc/Points/StandardCartesianChart3D/Positions Dataset
/T=1/adcirc/Edges Group
/T=1/adcirc/Edges/Points Group
/T=1/adcirc/Edges/Points/Positions Dataset
/T=1/adcirc/Faces Group
/T=1/adcirc/Faces/Points Group
/T=1/adcirc/Faces/Points/Positions Dataset
/T=1/adcirc/Connectivity Group
/T=1/adcirc/Connectivity/Points Group
/T=1/adcirc/Connectivity/Points/Positions Dataset
Index Depth 0
Index Depth = 1
Dimensionality 1
Dimensionality 2
Dimensionality 3

## Slide 87: Unstructured Meshes
Skeletons and Secondary Representations:
/T=1 Group
/T=1/adcirc Group
/T=1/adcirc/Points Group
/T=1/adcirc/Points/StandardCartesianChart3D Group
/T=1/adcirc/Points/StandardCartesianChart3D/Positions Dataset
/T=1/adcirc/Points/Faces Group
/T=1/adcirc/Points/Faces/Positions Dataset
/T=1/adcirc/Edges Group
/T=1/adcirc/Edges/Faces Group
/T=1/adcirc/Edges/Faces/Positions Dataset
/T=1/adcirc/Faces Group
/T=1/adcirc/Faces/Edges Group
/T=1/adcirc/Faces/Edges/Positions Dataset
/T=1/adcirc/Connectivity Group
/T=1/adcirc/Connectivity/Edges Group
/T=1/adcirc/Connectivity/Edges/Positions Dataset
Faces per Vertex
Faces per Edge
Edges per Face
Edges per Cell

## Slide 88: Hierarchical Meshes
One vertex may be covered by multiple refinement levels – multiresolution methods
Nested triangular grids for the La-Tex continental shelf (upper panel, Wang and Justic, 2009), the Breton Sound estuary (lower right panel, Huang et al., 2011) and (lower left) the Gulf of Mexico model.
Block-structured adaptive mesh refinement grid (AMR)

## Slide 89: Hierarchical Skeletons
Third identification parameter on Skeletons:
  “refinement” (integer valued or n-dimensional set of integer valued group attribute)
Allows to formulate “a grid within a grid”
Replicates topological structure on different refinement levels

## Slide 90: Skeletons as Fibers of a 3-dimensional parameter space
Index Depth
Dimensionality
Refinement

## Slide 91: Skeletons as Fibers of a 3-dimensional parameter space
Index Depth
Dimensionality
Refinement
Vertices

## Slide 92: Skeletons as Fibers of a 3-dimensional parameter space
Index Depth
Dimensionality
Refinement
Vertices
Edges
Sets of Edges
(Lines)
Faces
Sets of Faces
(Surface Regions)
Cells
Sets of Cells
(Blocks)
Vertex
Selection
Groups of Vertex
Selections

## Slide 93: Skeletons as Fibers of a 3-dimensional parameter space
Index Depth
Dimensionality
Refinement
Vertices
Edges
Sets of Edges
(Lines)
Faces
Sets of Faces
(Surface Regions)
Cells
Sets of Cells
(Blocks)
Vertex
Selection
Groups of Vertex
Selections
Vertices
Edges
Sets of Edges
(Lines)
Faces
Sets of Faces
(Surface Regions)
Cells
Sets of Cells
(Blocks)
Vertex
Selection
Groups of Vertex
Selections
Root
Level
1st
refinement
Level

## Slide 94: Relative Representations as Connectors between Skeletons
Index Depth
Dimensionality
Refinement
Vertices
Edges
Sets of Edges
(Lines)
Faces
Sets of Faces
(Surface Regions)
Cells
Sets of Cells
(Blocks)
Vertex
Selection
Groups of Vertex
Selections
Vertices
Edges
Sets of Edges
(Lines)
Faces
Sets of Faces
(Surface Regions)
Cells
Sets of Cells
(Blocks)
Vertex
Selection
Groups of Vertex
Selections
Root
Level
1st
refinement
Level

## Slide 95: Inter-Grid Relationships
Representations may refer to Skeletons within another Grid:
/T=0/FirstGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {1000}
/T=0/SecondGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {100}
?

## Slide 96: Inter-Grid Relationships
Use index fields/bitmaps when points match exactly:
Utilizes HDF5 symbolic links
/T=0/FirstGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {1000}
/T=0/FirstGrid/Points/SecondPoints/Positions {bitmap} Dataset {1000}
Representer  /T=0/SecondGrid/Points
/T=0/SecondGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {100}
/T=0/SecondGrid/Points/FirstPoints/Positions {int index} Dataset {100}
Representer  /T=0/FirstGrid/Points

## Slide 97: Inter-Grid Relationships
Use interpolation weights and indices when points do not match exactly:
Allows to evaluate any field on FirstGrid on SecondGrid (and vice versa)
/T=0/FirstGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {1000}
/T=0/FirstGrid/Points/SecondPoints/Positions {int [];} Dataset {1000}
Weights {float [];} Dataset {1000}
Representer  /T=0/SecondGrid/Points
/T=0/SecondGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {100}
/T=0/SecondGrid/Points/FirstPoints/Positions {int [];} Dataset {100}
Weights {float [];} Dataset {100}
Representer  /T=0/FirstGrid/Points

## Slide 98: Temporal Relationships
Representations may refer to Skeletons of the same Grid on different times:
Allows to trace the evolution of features
Timelike derivatives, …
/T=0/FirstGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {1000}
/T=0/FirstGrid/Points/SecondPoints/Positions {int [];} Dataset {1000}
Weights {float [];} Dataset {1000}
Representer  /T=1/FirstGrid/Points
/T=1/FirstGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {100}
/T=1/FirstGrid/Points/FirstPoints/Positions {int [];} Dataset {100}
Weights {float [];} Dataset {100}
Representer  /T=1/FirstGrid/Points

## Slide 99: Partial Time Dependence
Application Scenario:
  Curvilinear Grid with vector field
  Coordinates do not vary over time
  Dynamic Vector field, changes each time step
Utilizes HDF5 symbolic links
  Any application operation on dynamic data can read partially time-dependent data as well
  Any field can be defined time-independent, for all time steps, or just some time interval
/T=0/MyGrid/Points/CartesianChart3D/Positions {float x,y,z} Dataset {10,10,10}
/T=0/MyGrid/Points/CartesianChart3D/Vectorfield {float dx,dy,dz} Dataset {10,10,10}
/T=1/MyGrid/Points/CartesianChart3D/Positions  /T=0/MyGrid/Points/CartesianChart3D/Positions
/T=1/MyGrid/Points/CartesianChart3D/Vectorfield {float dx,dy,dz} Dataset {10,10,10}

## Slide 100: Summary
The F5 model avoids “keyword” conventions as much as possible
Semantic information is cast into the structure of the file instead of relying on naming conventions (enumeration approach, registries, naming standards…)
Interpretation of data fields is based on placement of data sets in the hierarchy
Internal layout is not 100% keyword-free, but as widely as possible
  Some keywords will become obsolete with future advancements of HDF5 (e.g., shared dataspaces)

## Slide 101: Conclusion
Commonalities across Grid types are not just enabled, they are unavoidable
Simple data types have simple representations
Complex data types are constructible from similar, reusable structures
The F5 model does not cover any type of data, but a very wide range
Certain aspects of the F5 model leave space for further refinement and definition how to interpret things

## Slide 102: F5 API
Implementation Design & Concepts

## Slide 103: Design of the F5 Library
API similar to HDF5
Expose HDF5, not hiding it
  Use as much of HDF5 as possible
  Upgrade to future HDF5 functionality once available
  Emulate future HDF5 functionality in the meanwhile

## Slide 104: Design of the F5 Library
3 categories of API functions:
  Internal API
    Common functions to share logistics
  Low-Level API
    Access to all constructions elements constituting the F5 formulation
  High-Level API
    Simple, “one-call” functions covering frequently asked cases

## Slide 105: F5Path object
Central object for user-accessible operations
This structure contains all HDF5 identifiers that describe a path in an HDF5 file towards a field structure.
/Time/Grid/Top/Rep/Field/Fragment
hid_t hid_t hid_t hid_t hid_t hid_t

## Slide 106: Example: API levels
F5Lwrite(hid_t R_id, const char*fieldname, int dimension, const hsize_t*dims, hid_t fieldtype, hid_t memtype, const void * dataPtr, hid_t enum_type, hid_t property_id);
F5Fwrite(F5Path*fpath, const char*fieldname, int dimension, hsize_t*dims, hid_t fieldtype, hid_t memtype, const void * dataPtr, hid_t property_id)
F5Fwrite_uniform_cartesian3D(hid_t file_id, double time, const char*gridname, const F5_vec3_point_t*origin, const F5_vec3_float_t*spacing, hsize_t dims[3], const char*fieldname, hid_t fieldtype, const void * dataPtr, const Char*coordinate_system,hid_t property_id);

## Slide 107: F5F.h
User Field Access Functions
  e.g.:
  F5Fwrite(F5Path*fpath, const char*fieldname, int dimension, hsize_t*dims, hid_t fieldtype, hid_t memtype, const void * dataPtr, hid_t property_id);
  Uses F5Path object to write HDF5 data to the right location
  Passes HDF5 information to the right location
  Performs additional semantic checks beyond HDF5 – dataspace consistent

## Slide 108: F5L.h
Internal low-level field functions
  E.g.:
  F5Lwrite(hid_t R_id, const char*fieldname, int dimension, const hsize_t*dims, hid_t fieldtype, hid_t memtype, const void * dataPtr, hid_t enum_type, hid_t property_id);
  Merely uses HDF5 identifiers
  Creates HDF5 dataset with attributes as interpreted by HDF5
  Caller must know exact location

## Slide 109: Groups of Functions
F5Bchart.h
  coordinate systems, charts
F5AMR.h
  adaptive mesh refinement
F5uniform.h
  Uniform meshes
…

## Slide 110: The End
http://www.hdfgroup.org
http://www.fiberbundle.net
http://sciviz.cct.lsu.edu/projects/vish/
http://f5.origo.ethz.ch